decoustics

"Suspended Accessible Reveal” Ceiling System (E)

SOLO M Type 8 VENEER FINISHED CEILING PANELS

Guide Specification

PART 1. GENERAL

1.01 Scope

A.	Include all labor, materials, and plant as required for the fabrication and delivery of acoustical ceiling panels for the system described and specified herein.

1.02 Related Work by Other

A.	Gypsum board partition, and wall and ceiling structure.

B.	Paint finish of ceiling surface behind and between panelling.

C.	Lighting fixtures and electrical services and connections.

D.	Air handling, heating and air conditioning, plumbing and other mechanical services as required.

E.	Public address system, speakers, wiring, support and installation.

F.	Life safety equipment.

G.	Ceilings by others not included in this scope.

1.03 Quality Assurance

A.	Manufacturer & Installer: Firm manufacturing the specified product shall have adequate capacity required for projects listed and have successfully completed similar projects for a period of not less than five years. The Installer should be approved by the Manufacturer as qualified to perform work required.

B.	Reference Standards:  Conform to all governing laws, building codes, and the following performance criteria:

1.	Fire Performance Characteristics: Provide acoustic ceiling panels with 			surface-burning characteristics as determined by testing panel components in 		accordance with ASTM E84 test procedures (building code requirements may 		necessitate composite panel testing using identical materials and construction 		representative of a typical installation, using the specified finish(es) - 			Decoustics has a considerable number of composite ASTM E84 panel tests 		on file). ASTM E-84 testing must be performed by a testing organization 			acceptable to authorities having jurisdiction.

ASTM E-84		Classification		      Class "A" or "1"

Flame Spread:		25 or less

Smoke Developed:		450 or less

2.	Acoustical Performance Characteristics:  Provide acoustical ceiling panels

with acoustical absorption characteristics as indicated in Part 2, which have

been determined by testing fully assembled production material in 				accordance with ASTM C-423 (Type "E400" mounting as defined by

ASTM E-795) by a testing organization acceptable to authorities having 			jurisdiction. Approved testing organization must be independent of the 			manufacturer.

3.	Ceiling panels shall have toxicity characteristics which have been determined by testing full assemblies (component tests are not acceptable) of identical materials and construction in accordance with section 27-348 of the New York State uniform fire prevention and building code MEA division.

MEA Acceptance Number 	MEA 183-06 M

1.04 Submittals

A.	Submit to the Architect of record, three (3) complete sets of CAD generated shop drawings prepared by the manufacturer showing all necessary details and dimension requirements which will subsequently be field verified and revised as required by the Architect.

B.	Samples: Submit (3 sets) manufacturers standard 8" (200mm) x 11" (280mm) sample panels of each type of product as specified in Part 2 to the Owner for approval.  Product shall be original production material in fabric finish specified for final use.

C.	Certification: Submit to the owner a certificate of compliance to specified acoustical and fire performance criteria as stated section 1.03 and Part 2 of this specification, signed by an officer of the panel manufacturer and attach independent laboratory test results for each product used, showing that the products supplied as components and complete assemblies, meet or exceed the specified requirements.

D.	Prior Approval:  Manufacturers not listed in section 2.01 of this specification and wishing to be submitted as an equal on the project must submit information in accordance with section 1.04 of this specification fifteen days prior to the bid date as outlined in the contract documents.  The information submitted must give evidence to show that the alternative product equals or exceeds the attributes and performance of the specified product.

E.	Manufacturers Approval:  The manufacturer shall have the right to approve the selection of the installing contractor and to verify that said contractor has sufficient experience and expertise to complete the project in a satisfactory manner.

F.	Single Source: All custom acoustical wall and ceiling panels shall be purchased from a single supplier.

1.05  Product Delivery, Storage and Handling

A.	Deliver fabricated units and related components to the site for installation in accordance with a reasonable schedule furnished by the contractor.  On-site storage shall be such as to assure that all panels and associated materials are protected from damage, and storage area is climatically controlled to normal operational levels..

B.	Prior to panel installation the site must be free of all wet and dusty trades and the climatic conditions stabilized to normal operational levels.  Panels shall be allowed to stabilize on site 24 hours prior to installation.

C.	Panels must only be handled by persons wearing clean light-weight gloves. It is very important that personnel installing hardware (clips, ceiling suspension systems, hanger wires, etc.) do not handle the panels before putting the clean lightweight gloves on.

1.06  Guarantee

A.	Furnish to the Architect in the Owner's name, the manufacturers written guarantee covering the products supplied against defects in materials and workmanship under normal operating conditions for a period of one year from the date of shipment.  Submit certificates of compliance showing warranty period by dates for each project completed to the Owner.

### PART 2 PRODUCTS

2.01	Acoustical Absorptive Ceiling Panel

Furnish and deliver prefabricated acoustical ceiling panels as described in this section for installation in areas as shown on drawings meeting or exceeding the following requirements:

Furnish and deliver prefabricated Decoustics Solo M Type 8 Acoustic Panels mounted using the "Suspended Accessible Reveal” ceiling system manufactured by:

Decoustics Limited

61 Royal Group Crescent,	 	TEL: (905) 652-5200

Woodbridge, Ontario.		 FAX: (905) 652-2505

Canada, L4H 1X9.			 Email: sales@decoustics.com

1.	The panels shall be comprised of a single piece MDF core of 16mm (5/8”) thickness faced with a real wood veneer. The structure is perforated by means of “V” routing on 8mm (5/16”) centers and intersecting perforations of 8mm (5/16”) diameter on 16mm (5/8”) centers. The panels shall be fabricated to sizes required by field dimensions supplied by the installing contractor and will not vary from determined sizes by more than +/- 3 mm (1/8") vertically and horizontally. The panels shall be supplied with a black facing on the back side. The panels shall be constructed using fire retardant core components meeting or exceeding Class A (Flame-spread of 25 or less and Smoke Developed of 450 or less) when tested in accordance with ASTM E-84 or UL-723 procedures.

2.	Veneer :

(A)	Select veneer from Manufacturers standard range of lacquer finished real wood veneers.

OR

B)	Architect / Designer specified finish

Source and laminate Architects specified veneer species, stained and lacquered to match Architects sample.

Unless otherwise specified, veneer will be quarter cut, slip matched. Veneer will not be sequenced.

Clear lacquer finish to 30% sheen.

3.	Installation shall be by use of DHC-25 clips field engaged into factory installed DPC-2 panel clips. This panel assembly is then suspended on the installer supplied frame/grid, by lifting up, across, and lowering. Panel clips (DPC-2 and DHC-25) shall be a minimum 20 gauge satin-coat steel. The DPC-2 clips shall be mechanically mounted to the back of the panels on nominal horizontal centres of 24" (610mm). Adhesively mounted clips are not acceptable.  All fasteners are to be supplied by the installing contractor. A minimum 1” (25 mm) reveal is required around all ceiling panels.

4.	Installation shall be in accordance with local code requirements, manufacturers’ instructions, and as shown on Decoustics approved shop drawings. Installer shall provide for adjustments as required to maintain consistent alignment of panels and of finished panel faces, and to ensure unstressed clip locations.

5.	Panels shall have noise reduction coefficient values of the following when tested in accordance with section 1.03 of this specification.

Frequency (Hz)

Panel Type		125	250	500	1000	2000	4000	NRC	SAA

SOLO M   	 	0.81	0.83	0.61	0.63	0.52	0.30	0.65	0.65

(No Core)

PART 3  INSPECTION AND APPROVAL

3.01  Adjustment and Replacement

A.	The Owner shall inspect the installation and product on completion. The manufacturer shall provide repair or replacement of components not conforming to requirements as stated herein, and said work will then become bound by the terms of this specification.

B.	Installation labor for removal and replacement of product improperly installed and not conforming to specified installation methods as detailed in section 2.01.3 and 2.01.4, and shown on approved shop drawings, shall be the responsibility of the installing Contractor.

- Solo is a real wood veneer product. Every effort is made to maintain the 	overall appearance, however, natural variations in grain, texture, shade and 	aging may occur in varying site conditions. For these reasons, the 	manufacturer cannot guarantee the exact matching of grain, pattern and 	color.