| SECTION 09510 / 09 51 00 CADRE ® and QUADRA ™ Ceiling Coffers |  | Product Specification |
| --- | --- | --- |

Copyright 1997, The American Institute of Architects (AIA)

This Section uses the term "Architect."  Change this term to match that used to identify the design professional as defined in the General and Supplementary Conditions.

Verify that Section titles referenced in this Section are correct for this Project's Specifications; Section titles may have changed.

GENERAL

RELATED DOCUMENTS

Drawings and general provisions of the Contract, including General and Supplementary Conditions and Division 1 Specification Sections, apply to this Section.

REFERENCES

ASTM C635, Standard Specifications for Metal Suspension Systems for Acoustical Tile and Lay-In Panel Ceilings.

ASTM C636, Recommended Practice for Installation of Metal Suspension System for Acoustical Tile and Lay-In Panels.

ATSM E84, Fire Hazard Classification.

CISCA Ceiling Systems Installation Handbook.

SUMMARY

This Section includes rigid, linear and curvilinear tees.

Related Sections include the following:

List below only products that the reader might expect to find in this Section but are specified elsewhere.

Division 9 – Section 09250 – Gypsum Board

Division 9 – Section 09511 – Acoustical Panel Ceilings

Division 15 Sections – Mechanical

Division 16 Sections – Electrical

SUBMITTALS

Samples: Submit panel finish and suspension system main and cross tees for acceptance.

Shop drawings:

Reflected ceiling plans: Submit ceiling system layout to indicate ceiling modules, and related lighting and mechanical systems.

Assembly drawings: Indicate module dimensions, accessory attachments, and installation of system components.

Manufacturer’s data:

System details: Submit manufacturer’s catalog cuts, literature, or standard drawings showing details of system with project conditions clearly identified and manufacturer’s recommended installation instructions.

Color chart: Submit manufacturer’s standard color chart sample or match of color choice for approval.

Maintenance materials: Provide _____ % of amount of main tees, cross tees, and panels.

DELIVERY, STORAGE, AND HANDLING

Delivery of materials: Deliver materials in original unopened packages, clearly labeled with manufacturer’s name, item description, specification number, type, and class, as applicable.

Inspection: Promptly inspect delivered materials, file freight claims for damage during shipment, and/or replacement materials, as required.

Storage: Ceiling material storage time at the jobsite should be as short as possible, and environmental conditions should be as near as possible to those specified for occupancy. (See Occupancy conditions below.) Excess humidity during storage can cause possible warp, sag, or poor fit after installation. Chemical changes in the reinforcement mat and/or coatings can be aggravated by excess humidity and cause discoloration during storage, even in unopened cartons. Cartons should be removed from pallets and stringers to prevent distortion of material. Damaged or deteriorated materials should be removed from the premises. Immediately before installation, to stabilize the ceiling coffers, store them at a location where temperature and humidity conditions duplicate ambient during installation and anticipated for occupancy.

Occupancy conditions: These ceiling coffers and suspension products are designed for installation and use under standard occupancy conditions of temperature and humidity 60-85 °F (16-29 °C), no more than 70% relative humidity (RH).

Handling: Handle in such a manner as to ensure against racking, distortion, or physical damage of any kind.

Retain subparagraphs below to suit Project or insert others.

QUALITY ASSURANCE

Subcontractor qualifications: Installer shall have not less than three years of successful experience in the installation of ceiling suspension systems on projects with requirements similar to requirements specified.

Requirements of regulatory agencies: Codes and regulations of authorities having jurisdiction.

Delete paragraph below if not required.  If retaining, indicate location, size, and other details of mockups on Drawings or by inserts.  Revise wording if only one mockup is required.

Source quality control: Manufacturer will provide test certification for ceiling system as required to meet industry performance standards specified by various agencies.

Delete below if work of this Section is not extensive or complex enough to justify a preinstallation conference.  If retaining, coordinate with Division 1 Section "Project Meetings."

Pre-installation Conference:  Conduct conference at Project site to comply with requirements in Division 1 Section "Project Meetings."

PROJECT CONDITIONS

Retain below for interior installations.

Existing conditions: (Include specific alteration work requirements for the project.)

Coordination with other work:

General: Coordinate with other work supported by or penetrating through the system.

Mechanical work: Ductwork above suspension system shall be complete, and permanent heating and cooling systems operating.

Electrical work: Installation of conduit above the CADRE ® and QUADRA ™ system shall be complete before installation of suspension system.

Protection:

Personnel: Follow good safety and industrial hygiene practices during handling and installing of all products and systems, with personnel to take necessary precautions, and wear appropriate personal protective equipment as needed. Read material safety data sheets and related literature for important information on products before installation. Contractor to be solely responsible for all personal safety issues during and subsequent to installation; architect, specifier, owner and manufacturer will rely on contractor’s performance in such regard.

Existing Completed Work: Protect completed work above suspension system from damage during installation of CADRE ® and QUADRA ™ system components.

SYSTEM DESCRIPTION
Suspended ceiling system consisting of main tees and cross tees connected together to form a modular installation for CADRE ® and QUADRA ™ , acoustical materials, light fixtures, and air diffusers.

Extra materials may not be allowed for publicly funded projects.

PRODUCTS

MANUFACTURER

In lieu of using schedule at the end of Part 3, insert names of products and manufacturers and revise paragraph above or below to suit Project.

CADRE and QUADRA Ceiling Systems and DONN ® (DX ® ) (DXT) (FINELINE ® ) (FINELINE 1/8) suspension systems as manufactured by USG Interiors, Inc., Chicago, Illinois, U.S.A.

B. Acoustical material shall be USG Interiors AURATONE ® ,ACOUSTONE ® , or ECLIPSE ™ ceiling panels or other, depending upon performance required (acoustical panels may not be required).

MATERIALS

CADRE and QUADRA ceiling panels:

Shall be manufactured from Glass Reinforced Gypsum (GRG) and formed into 24”x24” or 48”x48” lay-in panels. Panels are to be produced using Omni-directional glass reinforcement (chopper spray). No hand lay-up will be allowed.

Accessories:

M9 wall molding: 15/16”x9/16”x12’ -long angle shape of prepainted steel.

Panels with cutouts: For incandescent light, sprinklers, or speakers with integral trim to conceal the edge of the panel cutout (specify hole sizes and locations for each type), sized to fit the QUADRA top opening.

Suspension system components:

General: DONN (DX) (DXT) (FINELINE) (FINELINE 1/8): ASTM C635, (Intermediate) (Heavy Duty) classification, commercial quality cold-rolled steel; exposed surfaces pre-finished in manufacturer’s standard color.

Air distribution components:

DONN air diffusers: Extruded aluminum frame with flat white vanes (24”x24”) in (one) (two) (three) (four) slot configurations with four-directional throw. Finish to coordinate with CADRE and QUADRA panels.

Plenum: 28-gauge galvanized steel insulated with ½” fiberglass insulation, ____ DIA. top inlet collar.

In lieu of using schedule at the end of Part 3, delete paragraph below and insert product characteristics.

PERFORMANCE

Suspension system: (Intermediate) (Heavy Duty) classification designed to support ceiling assembly as indicated on project drawing with maximum deflection of 1/360.

Acoustical performance values are approximately the rating of the acoustical drop-in panels on all QUADRA.

Surface burning: Class A finished GRG surfaces shall have flame spread/smoke developed values of less than 0/15.

EXECUTION

EXAMINATION

Examine areas to receive materials for conditions that will adversely affect installation.

Do not start work until unsatisfactory conditions are corrected.

Work to be concealed: Verify work above ceiling system is complete and installed in manner that will not affect layout and installation of system components.

PREPARATION

Edit paragraph below to suit Project.

Field dimensions: Installer must verify actual field dimensions prior to installation.

Delete subparagraph below if not required.

INSTALLATION

Standard reference: Install in accordance with ASTM C636, CISCA recommendations and local building codes.

Manufacturer’s reference: Install in accordance with manufacturer’s current printed recommendations.

Drawing reference: Install in accordance with approved shop drawings.

Hanger wires:

Spacing: Space hanger wires on main tees a maximum of 48” o.c. attaching hangers directly to structure above.

Limitations: Do not support wires from mechanical and/or electrical equipment, piping, or other equipment occurring above ceiling.

Accessories: Install accessories as applicable to meet requirements.

Allowance tolerances: Per ASTM C636.

CLEANING

Maintenance: Perform any necessary cleaning maintenance with nonsolvent-based commercial cleaner on painted panels or suspension components.

Immediately remove any corrosive substances or chemicals that may attack finishes (e.g., wallpaper paste).

Removal of debris: Remove all debris resulting from work of this section.

Safety First!

Follow good safety and industrial hygiene practices during handling and installing of all products and systems. Take necessary precautions and wear the appropriate personal protective equipment as needed. Read material safety data sheets and related literature on products before specification and/or installation.

END OF SECTION 09510

**************************************************************************
The text material contained herein is intended for use as product reference material by architects, engineers, other design professionals, contractors, building code officials, or other competent construction industry trade factors having an interest in the selection, specification and use of products manufactured by the subsidiaries of USG Corporation. It is intended solely as technical support incident to the sale and use of our products.

These materials may be printed and/or transferred electronically as needed by the user. Modification of this information is the sole responsibility of the Design Professional. Any unauthorized duplication or reuse of the material contained herein is a violation of law.

**************************************************************************